## Slide 1: DATA PROTECTION AND PRIVACY TECHNOLOGIES FOR ENERGY
Presentation by:
ANTONIOS NTIB
CSP005_S_E
SLIDE SET #6: Hardware Security Module

## Slide 3: Outline
Crypto is great, but real-world security also needs hardware support
Design considerations and tradeoffs when designing hardware security modules

## Slide 4: Security Property and Crypto Primitives
Confidentiality
  Symmetric
  Asymmetric
Integrity
Freshness

## Slide 5: Symmetric Cryptography
How about encrypting arbitrary length message? Any problems?
One-time-pad (OTP)
Encryption:
ciphertext = key ⨁ plaintext
Decryption:
plaintext = key ⨁ ciphertext

## Slide 6: Block ciphers (e.g., DES, AES)
Divide data in blocks and encrypt/decrypt each block
AES block size can be 128, 192, 256 bits
ECB IS NOT RECOMMENDED

## Slide 7: Block ciphers (e.g., DES, AES)
IV can be public, but need to ensure to not reuse IV for the same key.
Real-world application: file/disk encryption and memory encryption. How to exchange the shared key between two parties?

## Slide 8: Asymmetric Cryptography (e.g., RSA)
A pair of keys:
  Private key (Kprivate – kept as secret)
  Public key (Kpublic – safe to release publicly)
Computation:
  Encrypt(plaintext, Kpublic) = ciphertext
  Decrypt(ciphertext, Kprivate) = plaintext
Computationally more expensive, so usually use asymmetric cryptography to negotiate a shared key (e.g., DKE key exchange), then use symmetric cryptography
How to announce and obtain the public key?
Mail box is public; Box key is private

## Slide 9: Public Key Infrastructures (PKIs)
Bob has a private key Kprivate and wants to claim he corresponds to a public key Kpublic
Analogy: public key is like a government-issued ID, need to be validated by an authority.
Certificate Authority
Alice
Bob
What is Bob’s public key?

## Slide 10: Public Key Infrastructures (PKIs)
Bob has a private key Kprivate and wants to claim he corresponds to a public key Kpublic
Analogy: public key is like a government-issued ID, need to be validated by an authority.
Establish a chain of trust
Real-world use cases: identify website, identify hardware chips/processors
Bob
Certificate Authority
Alice
Bob’s public key is Kpublic
Sign using the CA’s private key

## Slide 11: Integrity (MAC/Signature)
One-way hash
  Practically infeasible to invert, and difficult to find collision
Avalanche effect
  “Bob Smith got an A+ in ELE386 in Spring 2005”→ 01eace851b72386c46
  “Bob Smith got an B+ in ELE386 in Spring 2005”→ 936f8991c111f2cefaw
When message is long
  Divide message into blocks, and keep extending the hash by adding previous hash
Message (long)
Hash value (length depends on algorithm)
Hash(m) = h
Use as fingerprints

## Slide 12: Integrity + Crypto
Using symmetric crypto:
Using asymmetric crypto:
  Sign: sig = dec(hash, Kprivate)
  Verify:
    hash’= SHA(message)
    sig = enc(hash’, Kpublic)
hash | = | SHA(message)
HMAC | = | enc(hash, key)
Bob
Certificate Authority
Alice
Bob’s public key is Kpublic
Sign using the CA’s private key

## Slide 13: Freshness
Goal: to block replay attack
Bob
Certificate Authority
Alice
Bob’s public key is Kpublic_old
Sign using the CA’s private key

## Slide 14: Freshness
Goal: to block replay attack
Nounces + Integrity
  Nonce is a one-time use random number
  Should not reuse the same nounce
Alice
Bob
Certificate Authority
What is Bob’s public key?
+ Nounce

## Slide 15: Freshness
Goal: to block replay attack
Nounces + Integrity
  Nonce is a one-time use random number
  Should not reuse the same nounce
Challenge-response
Bob
Certificate Authority
Alice
Bob’s public key is Kpublic
+ Nounce
Sign using the CA’s private key

## Slide 16: Hardware establishes root of trust.
Security Contexts #1
work.
Lost
company’s highly-secure net
c) device, rootkits?
b) A remote server wants to trust anae)ndA-unseenr,de-u.gs.e, rwwhaentjsotinointrgusat a
remote server, e.g., bank server.

## Slide 17: Security Contexts #2
Software piracy (copying and reselling software to gain benefits).
Disk lost or removed, leading to confidentiality leakage.
Data encryption with weak passwords, such as, 6-digit passcode.
Bind data/application with hardware.

## Slide 18: Security Contexts #3
Remote computation where the host hypervisor and OS is not trusted.
Remote Computer managed by untrusted infrastructure provider
Software Provider Data Owner
Container runs trusted software
Hardware offers stronger isolation.

## Slide 19: What Can Hardware Security Modules Offer?
Establish root of trust
Bind data and applications with the hardware device
Offer stronger isolation
More efficient

## Slide 20: Secure Processors
Introduction to Security for Computer Architecture Students. Adam Hastings, Mohammed Tarek, Simha Sethumadhavan. https://www.cs.columbia.edu/~simha/ch1_supplement.pdf
19

## Slide 21: Before IBM 4758 (1999)
Crypto Accelerators
  Better performance
  Simple functionality
  Narrow interface
20
CPU
Crypto ASIC
(AES, RSA, etc.)

## Slide 22: IBM 4758 (1999) -- 4765 (2012)
Goal: a programmable, secure co-processor.
High level idea: virtual locker room
21
CPU
Programmable Secure
Co-processor
Stores the firmware and secret keys

## Slide 23: Software Layer Design and Concerns
Software stack:
  Application
  OS, kernel (microkernel)
  Loaders, firmware, etc.
Use cases:
  Solve music/software piracy issue
  Run an SSL server inside to store the agreed symmetric session keys
  Bank application
Problems:
  Update software is tricky
  Bad programmability due to microkernel

## Slide 24: Compare to TrustZone
IBM 4758
CPU
Programmable Secure
Co-processor
ARM TrustZone

## Slide 25: Trusted Platform Module (TPM)
“Commoditized IBM 4758”
Standard LPC interface – attaches to commodity motherboards
Weaker computation capability
Use cases:
  Disk encryption and password protection (“seal”)
  Verify platform integrity (firmware+OS)

## Slide 26: Boot Process (UEFI)
How to perform the measurement?

## Slide 27: Secure Boot using TPM
PCR: platform configuration register

## Slide 28: Open-source Choice: Google Titan
from https://www.hotchips.org/hc30/1conf/1.14_Google_Titan_GoogleFinalTitanHotChips2018.pdf

## Slide 29: Security Problems of Using TPM
Assume the first-stage bootloader is securely embedded in motherboard
Not easy to use with frequent software/kernel update
Time to check, time to use
TPM Reset attacks
exploiting software vulnerabilities and using software to report false hash values
Han et al. A Bad Dream: Subverting Trusted Platform Module While You Are Sleeping. Usenix Security’18 Wojtczuk et al. Attacking Intel TXT® via SINIT code execution hijacking. 2011
Root of trust
CPU
TPM

## Slide 30: Apple Secure Enclave
Additional Goals:
Prevent jailbreak
Easy to use
Advantage: one company controls both the hardware and the software

## Slide 31: Isolation
Why separate cores?
Similar to IBM 4758
Strong isolation
Block vulnerabilities due to software bugs (running L4 microkernel) and side channels
Different from IBM 4758
Not general-purpose, only run secure enclave functionality

## Slide 32: Crypto Keys
The Secure Enclave includes a unique ID (UID) root cryptographic key.
Unique to each device
Randomly generated
Fused into the SoC at manufacturing time
Not visible outside the device

## Slide 33: Secure Non-volatile Storage
For easy to use: short passcode. But weaker security?
Passcode + UID -> passcode entropy
Brute-force has to be performed on the device under attack
Escalating time delays
Erase data when exceeding attempt count
All user data encryption keys

## Slide 34: Secure Boot
Similar to TPM but with more constraints
Each step is signed by Apple to prevent loading non-Apple systems
  Using Apple Root Certificate authority public key
Verify more components, including
operating system, kernel extensions, etc.
Keep track of version number to prevent rolling back to older/vulnerable versions

## Slide 35: Summary
What Can Hardware Security Modules Offer?
  Establish root of trust
  Bind data and applications with the hardware device
  Offer stronger isolation
  More efficient

## Slide 36: Thank you